PUG MILL OPERATIONS

1. Load Clay into Mixing Chamber.

2. Clean excess clay from lid seal.

3. Mix for 3 Minutes.

4. STOP MIX.

5. Run Pug mode for 7 seconds.

6. STOP PUG.

7. Run air pump until dial reads past 25.

8. Stop air pump.

9. Pug clay.

10. STOP PUG.

11. Open air release valve.

12. Let air drop to 0.

13. Close air release valve.

14. Start again.